Sugiyama Layout
A Rosetta Stone for the that Sugiyama Graph Drawing Paper
# The Graph used as an Example.

a
b
c
d
e
f
g
h
i
j
k
l
m

# II: Basic Definitions
## A: n-Level Hierarchy and Map
For a graph G(V, E), V is the set of vertices and E is the set of edges.

V is partitioned into n subsets, that is
V = V_{1} ` union ` V_{2} ` union ` dotsaxis ` union ` V_{n}~~(V_{i} ` intersection ` V_{j} ` = ` emptyset , ` i ` <> ` j )
The graph is layered. There are n layers. Vertices are on one layer and one layer only. Likewise, the edges are seperated into sets of edges which connect each layer:
 E = E_{1} ` union ` E_{2} ` union ` dotsaxis ` union ` E_{n-1}~~(E_{i} ` intersection ` E_{j} ` = ` emptyset , ` i ` <> ` j )

An order σi of Vi is given for each i, where the term “order” means a sequence of all vertices of Vi;
σ _{1} = v_{1}, v_{2}, dotsaxis , v_{ abs{ V_{i} } }
The order of the vertices in each layer is important. For the example graph:
%sigma_{1} = ( a, b, c ) newline %sigma_{2} = ( c, d, e, f ) newline %sigma_{3} = ( g, h, i, j ) newline %sigma_{4} = ( k, l, m )
The drawing of a hierarchy is called a 'map'.

So, Python-wise, for the example graph, we've something like:
V = [ list('ab') , list('cdef'), list('ghij'), list('klm') ]
E = [ [('a','c'), ('a','d'), ('a','e'), ('a','f'), ('b','c'), ('b','f') ],
       [('c','g'), ('d','h'), ('d','i'), ('d','j'), ('e','g'), ('e','j') ],
       [('g','k'), ('i','k'), ('i','m'), ('j','k'), ('j','l') ]
    ]

levels = len(V)
## B: Matrix Realisation of n-Level Hierarchies
A matrix M(i) = M(σi, σi+1) is a |Vi| x |Vi+1| matrix whose rows and columns are ordered according to σi and σi+1 respectively.
We're building a matrix for each layer in the graph. Rows are sources, columns are sinks. Vertices which are connected get a '1' in this matrix and unconnected vertices get a '0'. There is one less matrix that there are layers. For the example graph:
M_{1} `=` matrix { {} # matrix { c # d # e# f } ## stack{ a # b } # left [ matrix{1 # 1 # 1 # 1 ## 1 # 0 # 0 # 1} right ] } ~~ M_{2} `=` matrix { {} # matrix { g # h# i# j } ## stack { c#d#e#f} # left [ matrix{ 1 # 0 # 0 # 0 ## 0 # 1 # 1 # 1 ## 1 # 0 # 0 # 1 ## 0 # 0 # 0 # 0 } right ] } ~~ M_{3} `=` matrix { {} # matrix { k#l#m} ## stack {g#h#i#j} # left [ matrix { 1 # 0 # 0 ## 0 # 0 # 0 ## 1 # 0 # 1 ## 1 # 1 # 0 } right ] }

M = []
for i in xrange(levels-1):
    m_shape = ( len( V[i] ), len( V[i+1] ) )
    m = zeros( m_shape )

    for e in E[i]:
        row = V[i].index( e[0] )
        col = V[i+1].index( e[1] )
        m[row][col] = 1

    M.append(m)

A matrix realisation g of G is given by the formula g(σi, ..., σn) = M(1) ... M(n-1)

## C: The Number of Crossings of n-Level Hierarchies
In the i th interconnection matrix M^{(i)} ` = ` M( %sigma_{i}, %sigma_{i+1}) of g, let %sigma_{i} ` = ` v_{1} dotsaxis v_{j} dotsaxis v_{k} dotsaxis v_{abs{V_{i}}} . Further, let the row vector of M^{(i)} corresponding to a vertex v in V_{i} be denoted by r(v), then the number of crossings k( r(v_{j}), r(v_{k}) ) produced by the ordered pair of row vectors (r(v_{j}), r(v_{k})) is given by the formula
k( r(v_{j}), r(v_{k}) ) = sum from { %alpha = 1 } to { q-1 } { sum from { %beta = %alpha + 1 } to {q} { m^{(i)}_{j%beta} m^{(i)}_{k%alpha} } } where q = abs{V_{i+1}}
Taking into account Python's zero-indexing carry on:
def calc_k(i,j,k):
    """ Calculate the crossings between an ordered pair of vertex rows. """
    q = len( V[i+1] )
    k_jk = 0

    for a in xrange(0,q-1): # 0 ... q-2
        for b in xrange(a+1, q): # a+1 ... q -1
        k_jk += M[i][j][b] * M[i][k][a]

    return k_jk

Crossovers... So, to get the crossovers in each layer, we have to check crossovers between each row vector in the layer. Hence:
sum from { j = 1 } to { p-1 } { sum from { k = j + 1 } to {p} { k( r(v_{j}), r(v_{k}) ) } } where p = abs{V_{i}}
Which in Python is:
def calc_layer_crossings(i):
    p = len( V[i] )
    K_M = 0

    for j in xrange(0,p-1):
        for k in xrange(j+1,p):
        K_M += calc_k(i, j, k )

    return K_M

adfsa

So far, our Python program outputs the interconnection matrices and the crossover count for each layer:
M(0)
[[ 1. 1. 1. 1.]
 [ 1. 0. 0. 1.]]

M(1)
[[ 1. 0. 0. 0.]
 [ 0. 1. 1. 1.]
 [ 1. 0. 0. 1.]
 [ 0. 0. 0. 0.]]

M(2)
[[ 1. 0. 0.]
 [ 0. 0. 0.]
 [ 1. 0. 1.]
 [ 1. 1. 0.]]

Layer 0 3.0
Layer 1 3.0
Layer 2 2.0

## D: Connectivity
In an n-level hierarchy G = (V,E,n,%sigma) if %sigma_{i} = v^{i}_{1} dotsaxis v^{i}_{k} dotsaxis v^{i}_{abs{V_{i}}} , i=1,dotsaxis,n , then the upper connectivity C^{U}_{ik} of vertex v^{i}_{k} and the lower connectivity C^{L}_{ik} of vertex v^{i}_{k} are defined by the formulas
C^{U}_{ik} = sum from {j=1} to {abs{V_{i-1}}} {m^{i-1}_{jk} } ~~~~ k = 1, dotsaxis, abs{V_{i}}, ~~~~ i = 2, dotsaxis, n
C^{L}_{ik} = sum from {l=1} to {abs{V_{i+1}}} {m^{i}_{kl} } ~~~~ k = 1, dotsaxis, abs{V_{i}}, ~~~~ i = 1, dotsaxis, n-1
For each vertice, we're counting how many vertices its connected to in the layer above. We get a count for connections to the layer below too.
def calc_upper_connectivity( i, k ):
    lim = len( V[i-1] )
    C_U = 0

    for j in xrange(0, lim ):
        C_U += M[i-1][j][k]

    return C_U

def calc_lower_connectivity( i, k ):
    lim = len( V[i+1] )
    C_L = 0

    for l in xrange(0, lim ):
        C_L += M[i][k][l]

    return C_L
## E: Barycentres