Verilog 2001 Formal Syntax Definition
The formal syntax of Verilog HDL is described
using Backus-Naur Form (BNF).

# A.1 Source text
## A.1.1 Library source text
library_text ::= { library_descriptions }
library_descriptions ::=
        library_declaration
      | include_statement
      | config_declaration
library_declaration ::=
        library library_identifier file_path_spec [ { , file_path_spec } ]
        [ -incdir file_path_spec [ { , file_path_spec } ] ;
file_path_spec ::= file_path
include_statement ::= include <file_path_spec> ;
## A.1.2 Configuration source text
config_declaration ::=
        config config_identifier ;
        design_statement
        {config_rule_statement}
        endconfig
design_statement ::= design { [library_identifier.]cell_identifier } ;
config_rule_statement ::=
        default_clause liblist_clause
      | inst_clause liblist_clause
      | inst_clause use_clause
      | cell_clause liblist_clause
      | cell_clause use_clause
default_clause ::= default
inst_clause ::= instance inst_name
inst_name ::= topmodule_identifier{.instance_identifier}
cell_clause ::= cell [ library_identifier.]cell_identifier
liblist_clause ::= liblist [{library_identifier}]
use_clause ::= use [library_identifier.]cell_identifier[:config]

## A.1.3 Module and primitive source text
 source_text ::= { description }
 description ::=
        module_declaration
       | udp_declaration
 module_declaration ::=
        { attribute_instance } module_keyword module_identifier [ module_parameter_port_list ]
        [ list_of_ports ] ; { module_item }
        endmodule
       | { attribute_instance } module_keyword module_identifier [ module_parameter_port_list ]
        [ list_of_port_declarations ] ; { non_port_module_item }
        endmodule
 module_keyword ::= module | macromodule
## A.1.4 Module parameters and ports
module_parameter_port_list ::= # ( parameter_declaration { , parameter_declaration } )
list_of_ports ::= ( port { , port } )
list_of_port_declarations ::=
        ( port_declaration { , port_declaration } )
       |()
port ::=
        [ port_expression ]
       | . port_identifier ( [ port_expression ] )
port_expression ::=
        port_reference
       | { port_reference { , port_reference } }
port_reference ::=
        port_identifier
       | port_identifier [ constant_expression ]
       | port_identifier [ range_expression ]
port_declaration ::=
        {attribute_instance} inout_declaration
       | {attribute_instance} input_declaration
       | {attribute_instance} output_declaration
## A.1.5 Module items
module_item ::=
        module_or_generate_item
       | port_declaration ;
       | { attribute_instance } generated_instantiation
       | { attribute_instance } local_parameter_declaration
       | { attribute_instance } parameter_declaration
       | { attribute_instance } specify_block
       | { attribute_instance } specparam_declaration
module_or_generate_item ::=
       { attribute_instance } module_or_generate_item_declaration
     | { attribute_instance } parameter_override
     | { attribute_instance } continuous_assign
     | { attribute_instance } gate_instantiation
     | { attribute_instance } udp_instantiation
     | { attribute_instance } module_instantiation
     | { attribute_instance } initial_construct
     | { attribute_instance } always_construct
module_or_generate_item_declaration ::=
       net_declaration
     | reg_declaration
     | integer_declaration
     | real_declaration
     | time_declaration
     | realtime_declaration
     | event_declaration
     | genvar_declaration
     | task_declaration
     | function_declaration
non_port_module_item ::=
       { attribute_instance } generated_instantiation
     | { attribute_instance } local_parameter_declaration
     | { attribute_instance } module_or_generate_item
     | { attribute_instance } parameter_declaration
     | { attribute_instance } specify_block
     | { attribute_instance } specparam_declaration
parameter_override ::= defparam list_of_param_assignments ;
# A.2 Declarations
## A.2.1 Declaration types
### A.2.1.1 Module parameter declarations
local_parameter_declaration ::=
       localparam [ signed ] [ range ] list_of_param_assignments ;
     | localparam integer list_of_param_assignments ;
     | localparam real list_of_param_assignments ;
     | localparam realtime list_of_param_assignments ;
     | localparam time list_of_param_assignments ;
parameter_declaration ::=
       parameter [ signed ] [ range ] list_of_param_assignments ;
     | parameter integer list_of_param_assignments ;
     | parameter real list_of_param_assignments ;
     | parameter realtime list_of_param_assignments ;
     | parameter time list_of_param_assignments ;
specparam_declaration ::= specparam [ range ] list_of_specparam_assignments ;
### A.2.1.2 Port declarations
inout_declaration ::= inout [ net_type ] [ signed ] [ range ]
        list_of_port_identifiers
input_declaration ::= input [ net_type ] [ signed ] [ range ]
        list_of_port_identifiers
output_declaration ::=
        output [ net_type ] [ signed ] [ range ]
        list_of_port_identifiers
       | output [ reg ] [ signed ] [ range ]
        list_of_port_identifiers
       | output reg [ signed ] [ range ]
        list_of_variable_port_identifiers
       | output [ output_variable_type ]
        list_of_port_identifiers
       | output output_variable_type
        list_of_variable_port_identifiers
### A.2.1.3 Type declarations
event_declaration ::= event list_of_event_identifiers ;
genvar_declaration ::= genvar list_of_genvar_identifiers ;
integer_declaration ::= integer list_of_variable_identifiers ;
net_declaration ::=
        net_type [ signed ]
        [ delay3 ] list_of_net_identifiers ;
       | net_type [ drive_strength ] [ signed ]
        [ delay3 ] list_of_net_decl_assignments ;
       | net_type [ vectored | scalared ] [ signed ]
        range [ delay3 ] list_of_net_identifiers ;
       | net_type [ drive_strength ] [ vectored | scalared ] [ signed ]
        range [ delay3 ] list_of_net_decl_assignments ;
       | trireg [ charge_strength ] [ signed ]
        [ delay3 ] list_of_net_identifiers ;
       | trireg [ drive_strength ] [ signed ]
        [ delay3 ] list_of_net_decl_assignments ;
       | trireg [ charge_strength ] [ vectored | scalared ] [ signed ]
        range [ delay3 ] list_of_net_identifiers ;
       | trireg [ drive_strength ] [ vectored | scalared ] [ signed ]
        range [ delay3 ] list_of_net_decl_assignments ;
real_declaration ::= real list_of_real_identifiers ;
realtime_declaration ::= realtime list_of_real_identifiers ;
reg_declaration ::= reg [ signed ] [ range ]
        list_of_variable_identifiers ;
time_declaration ::= time list_of_variable_identifiers ;
## A.2.2 Declaration data types
### A.2.2.1 Net and variable types
net_type ::=
        supply0 | supply1
      | tri | triand | trior | tri0 | tri1
      | wire | wand | wor
output_variable_type ::= integer | time
real_type ::=
        real_identifier [ = constant_expression ]
      | real_identifier dimension { dimension }
variable_type ::=
        variable_identifier [ = constant_expression ]
      | variable_identifier dimension { dimension }
### A.2.2.2 Strengths
drive_strength ::=
        ( strength0 , strength1 )
      | ( strength1 , strength0 )
      | ( strength0 , highz1 )
      | ( strength1 , highz0 )
      | ( highz0 , strength1 )
      | ( highz1 , strength0 )
strength0 ::= supply0 | strong0 | pull0 | weak0
strength1 ::= supply1 | strong1 | pull1 | weak1
charge_strength ::= ( small ) | ( medium ) | ( large )
### A.2.2.3 Delays
delay3 ::= # delay_value | # ( delay_value [ , delay_value [ , delay_value ] ] )
delay2 ::= # delay_value | # ( delay_value [ , delay_value ] )
delay_value ::=
        unsigned_number
      | parameter_identifier
      | specparam_identifier
      | mintypmax_expression
## A.2.3 Declaration lists
list_of_event_identifiers ::= event_identifier [ dimension { dimension }]
        { , event_identifier [ dimension { dimension }] }
list_of_genvar_identifiers ::= genvar_identifier { , genvar_identifier }
list_of_net_decl_assignments ::= net_decl_assignment { , net_decl_assignment }
list_of_net_identifiers ::= net_identifier [ dimension { dimension }]
        { , net_identifier [ dimension { dimension }] }
list_of_param_assignments ::= param_assignment { , param_assignment }
list_of_port_identifiers ::= port_identifier { , port_identifier }
list_of_real_identifiers ::= real_type { , real_type }
list_of_specparam_assignments ::= specparam_assignment { , specparam_assignment }
list_of_variable_identifiers ::= variable_type { , variable_type }
list_of_variable_port_identifiers ::= port_identifier [ = constant_expression ]
        { , port_identifier [ = constant_expression ] }

## A.2.4 Declaration assignments
net_decl_assignment ::= net_identifier = expression
param_assignment ::= parameter_identifier = constant_expression
specparam_assignment ::=
        specparam_identifier = constant_mintypmax_expression
      | pulse_control_specparam
pulse_control_specparam ::=
        PATHPULSE$ = ( reject_limit_value [ , error_limit_value ] ) ;
      | PATHPULSE$specify_input_terminal_descriptor$specify_output_terminal_descriptor
        = ( reject_limit_value [ , error_limit_value ] ) ;
error_limit_value ::= limit_value
reject_limit_value ::= limit_value
limit_value ::= constant_mintypmax_expression
## A.2.5 Declaration ranges
dimension ::= [ dimension_constant_expression : dimension_constant_expression ]
range ::= [ msb_constant_expression : lsb_constant_expression ]
## A.2.6 Function declarations
function_declaration ::=
        function [ automatic ] [ signed ] [ range_or_type ] function_identifier ;
        function_item_declaration { function_item_declaration }
        function_statement
        endfunction
        | function [ automatic ] [ signed ] [ range_or_type ] function_identifier ( function_port_list ) ;
        block_item_declaration { block_item_declaration }
        function_statement
        endfunction
function_item_declaration ::=
        block_item_declaration
      | tf_input_declaration ;
function_port_list ::= { attribute_instance } tf_input_declaration { , { attribute_instance }
        tf_input_declaration }
range_or_type ::= range | integer | real | realtime | time
## A.2.7 Task declarations
task_declaration ::=
        task [ automatic ] task_identifier ;
        { task_item_declaration }
        statement
        endtask
        | task [ automatic ] task_identifier ( task_port_list ) ;
        { block_item_declaration }
        statement
        endtask
task_item_declaration ::=
        block_item_declaration
      | { attribute_instance } tf_input_declaration ;
      | { attribute_instance } tf_output_declaration ;
      | { attribute_instance } tf_inout_declaration ;
task_port_list ::= task_port_item { , task_port_item }
task_port_item ::=
        { attribute_instance } tf_input_declaration
      | { attribute_instance } tf_output_declaration
      | { attribute_instance } tf_inout_declaration
tf_input_declaration ::=
        input [ reg ] [ signed ] [ range ] list_of_port_identifiers
      | input [ task_port_type ] list_of_port_identifiers
tf_output_declaration ::=
        output [ reg ] [ signed ] [ range ] list_of_port_identifiers
      | output [ task_port_type ] list_of_port_identifiers
tf_inout_declaration ::=
        inout [ reg ] [ signed ] [ range ] list_of_port_identifiers
      | inout [ task_port_type ] list_of_port_identifiers
task_port_type ::=
        time | real | realtime | integer
## A.2.8 Block item declarations
block_item_declaration ::=
        { attribute_instance } block_reg_declaration
      | { attribute_instance } event_declaration
      | { attribute_instance } integer_declaration
      | { attribute_instance } local_parameter_declaration
      | { attribute_instance } parameter_declaration
      | { attribute_instance } real_declaration
      | { attribute_instance } realtime_declaration
      | { attribute_instance } time_declaration
block_reg_declaration ::= reg [ signed ] [ range ]
        list_of_block_variable_identifiers ;
list_of_block_variable_identifiers ::=
        block_variable_type { , block_variable_type }
block_variable_type ::=
        variable_identifier
      | variable_identifier dimension { dimension }

# A.3 Primitive instances
## A.3.1 Primitive instantiation and instances
gate_instantiation ::=
        cmos_switchtype [delay3]
        cmos_switch_instance { , cmos_switch_instance } ;
      | enable_gatetype [drive_strength] [delay3]
        enable_gate_instance { , enable_gate_instance } ;
      | mos_switchtype [delay3]
        mos_switch_instance { , mos_switch_instance } ;
      | n_input_gatetype [drive_strength] [delay2]
        n_input_gate_instance { , n_input_gate_instance } ;
      | n_output_gatetype [drive_strength] [delay2]
        n_output_gate_instance { , n_output_gate_instance } ;
      | pass_en_switchtype [delay2]
        pass_enable_switch_instance { , pass_enable_switch_instance } ;
      | pass_switchtype
        pass_switch_instance { , pass_switch_instance } ;
      | pulldown [pulldown_strength]
        pull_gate_instance { , pull_gate_instance } ;
      | pullup [pullup_strength]
        pull_gate_instance { , pull_gate_instance } ;
cmos_switch_instance ::= [ name_of_gate_instance ] ( output_terminal , input_terminal ,
        ncontrol_terminal , pcontrol_terminal )
enable_gate_instance ::= [ name_of_gate_instance ] ( output_terminal , input_terminal , enable_terminal )
mos_switch_instance ::= [ name_of_gate_instance ] ( output_terminal , input_terminal , enable_terminal )
n_input_gate_instance ::= [ name_of_gate_instance ] ( output_terminal , input_terminal { , input_terminal } )
n_output_gate_instance ::= [ name_of_gate_instance ] ( output_terminal { , output_terminal } ,
        input_terminal )
pass_switch_instance ::= [ name_of_gate_instance ] ( inout_terminal , inout_terminal )
pass_enable_switch_instance ::= [ name_of_gate_instance ] ( inout_terminal , inout_terminal ,
        enable_terminal )
pull_gate_instance ::= [ name_of_gate_instance ] ( output_terminal )
name_of_gate_instance ::= gate_instance_identifier [ range ]
## A.3.2 Primitive strengths
pulldown_strength ::=
        ( strength0 , strength1 )
      | ( strength1 , strength0 )
      | ( strength0 )
pullup_strength ::=
        ( strength0 , strength1 )
      | ( strength1 , strength0 )
      | ( strength1 )
## A.3.3 Primitive terminals
enable_terminal ::= expression
inout_terminal ::= net_lvalue
input_terminal ::= expression
ncontrol_terminal ::= expression
output_terminal ::= net_lvalue
pcontrol_terminal ::= expression
## A.3.4 Primitive gate and switch types
cmos_switchtype ::= cmos | rcmos
enable_gatetype ::= bufif0 | bufif1 | notif0 | notif1
mos_switchtype ::= nmos | pmos | rnmos | rpmos
n_input_gatetype ::= and | nand | or | nor | xor | xnor
n_output_gatetype ::= buf | not
pass_en_switchtype ::= tranif0 | tranif1 | rtranif1 | rtranif0
pass_switchtype ::= tran | rtran
# A.4 Module and generated instantiation
## A.4.1 Module instantiation
module_instantiation ::=
        module_identifier [ parameter_value_assignment ]
        module_instance { , module_instance } ;
parameter_value_assignment ::= # ( list_of_parameter_assignments )
list_of_parameter_assignments ::=
      ordered_parameter_assignment { , ordered_parameter_assignment } |
      named_parameter_assignment { , named_parameter_assignment }
ordered_parameter_assignment ::= expression
named_parameter_assignment ::= . parameter_identifier ( [ expression ] )
module_instance ::= name_of_instance ( [ list_of_port_connections ] )
name_of_instance ::= module_instance_identifier [ range ]
list_of_port_connections ::=
        ordered_port_connection { , ordered_port_connection }
      | named_port_connection { , named_port_connection }
ordered_port_connection ::= { attribute_instance } [ expression ]
named_port_connection ::= { attribute_instance } .port_identifier ( [ expression ] )
## A.4.2 Generated instantiation
generated_instantiation ::= generate { generate_item } endgenerate
generate_item_or_null ::= generate_item | ;
generate_item ::=
        generate_conditional_statement
      | generate_case_statement
      | generate_loop_statement
      | generate_block
      | module_or_generate_item
 generate_conditional_statement ::=
        if ( constant_expression ) generate_item_or_null [ else generate_item_or_null ]
 generate_case_statement ::= case ( constant_expression )
        genvar_case_item { genvar_case_item } endcase
 genvar_case_item ::= constant_expression { , constant_expression } :
        generate_item_or_null | default [ : ] generate_item_or_null
 generate_loop_statement ::= for ( genvar_assignment ; constant_expression ; genvar_assignment )
        begin : generate_block_identifier { generate_item } end
 genvar_assignment ::= genvar_identifier = constant_expression
 generate_block ::= begin [ : generate_block_identifier ] { generate_item } end
# A.5 UDP declaration and instantiation
## A.5.1 UDP declaration
udp_declaration ::=
        { attribute_instance } primitive udp_identifier ( udp_port_list ) ;
        udp_port_declaration { udp_port_declaration }
        udp_body
        endprimitive
        | { attribute_instance } primitive udp_identifier ( udp_declaration_port_list ) ;
        udp_body
        endprimitive
## A.5.2 UDP ports
udp_port_list ::= output_port_identifier , input_port_identifier { , input_port_identifier }
udp_declaration_port_list ::=
      udp_output_declaration , udp_input_declaration { , udp_input_declaration }
udp_port_declaration ::=
        udp_output_declaration ;
      | udp_input_declaration ;
      | udp_reg_declaration ;
udp_output_declaration ::=
        { attribute_instance } output port_identifier
      | { attribute_instance } output reg port_identifier [ = constant_expression ]
udp_input_declaration ::= { attribute_instance } input list_of_port_identifiers
udp_reg_declaration ::= { attribute_instance } reg variable_identifier
## A.5.3 UDP body
udp_body ::= combinational_body | sequential_body
combinational_body ::= table combinational_entry { combinational_entry } endtable
combinational_entry ::= level_input_list : output_symbol ;
sequential_body ::= [ udp_initial_statement ] table sequential_entry { sequential_entry } endtable
udp_initial_statement ::= initial output_port_identifier = init_val ;
init_val ::= 1’b0 | 1’b1 | 1’bx | 1’bX | 1’B0 | 1’B1 | 1’Bx | 1’BX | 1 | 0
sequential_entry ::= seq_input_list : current_state : next_state ;
seq_input_list ::= level_input_list | edge_input_list
level_input_list ::= level_symbol { level_symbol }
edge_input_list ::= { level_symbol } edge_indicator { level_symbol }
edge_indicator ::= ( level_symbol level_symbol ) | edge_symbol
current_state ::= level_symbol
next_state ::= output_symbol | -
output_symbol ::= 0 | 1 | x | X
level_symbol ::= 0 | 1 | x | X | ? | b | B
edge_symbol ::= r | R | f | F | p | P | n | N | *
## A.5.4 UDP instantiation
udp_instantiation ::= udp_identifier [ drive_strength ] [ delay2 ]
        udp_instance { , udp_instance } ;
udp_instance ::= [ name_of_udp_instance ] ( output_terminal , input_terminal
        { , input_terminal } )
name_of_udp_instance ::= udp_instance_identifier [ range ]
# A.6 Behavioral statements
## A.6.1 Continuous assignment statements
continuous_assign ::= assign [ drive_strength ] [ delay3 ] list_of_net_assignments ;
list_of_net_assignments ::= net_assignment { , net_assignment }
net_assignment ::= net_lvalue = expression
## A.6.2 Procedural blocks and assignments
initial_construct ::= initial statement
always_construct ::= always statement
blocking_assignment ::= variable_lvalue = [ delay_or_event_control ] expression
nonblocking_assignment ::= variable_lvalue <= [ delay_or_event_control ] expression
procedural_continuous_assignments ::=
        assign variable_assignment
      | deassign variable_lvalue
      | force variable_assignment
      | force net_assignment
      | release variable_lvalue
      | release net_lvalue
 function_blocking_assignment ::= variable_lvalue = expression
 function_statement_or_null ::=
        function_statement
      | { attribute_instance } ;
## A.6.3 Parallel and sequential blocks
function_seq_block ::= begin [ : block_identifier
        { block_item_declaration } ] { function_statement } end
variable_assignment ::= variable_lvalue = expression
par_block ::= fork [ : block_identifier
        { block_item_declaration } ] { statement } join
seq_block ::= begin [ : block_identifier
        { block_item_declaration } ] { statement } end
## A.6.4 Statements
statement ::=
        { attribute_instance } blocking_assignment ;
      | { attribute_instance } case_statement
      | { attribute_instance } conditional_statement
      | { attribute_instance } disable_statement
      | { attribute_instance } event_trigger
      | { attribute_instance } loop_statement
      | { attribute_instance } nonblocking_assignment ;
      | { attribute_instance } par_block
      | { attribute_instance } procedural_continuous_assignments ;
      | { attribute_instance } procedural_timing_control_statement
      | { attribute_instance } seq_block
      | { attribute_instance } system_task_enable
      | { attribute_instance } task_enable
      | { attribute_instance } wait_statement
statement_or_null ::=
        statement
      | { attribute_instance } ;
function_statement ::=
        { attribute_instance } function_blocking_assignment ;
      | { attribute_instance } function_case_statement
      | { attribute_instance } function_conditional_statement
      | { attribute_instance } function_loop_statement
      | { attribute_instance } function_seq_block
      | { attribute_instance } disable_statement
      | { attribute_instance } system_task_enable
## A.6.5 Timing control statements
delay_control ::=
        # delay_value
      | # ( mintypmax_expression )
delay_or_event_control ::=
       delay_control
     | event_control
     | repeat ( expression ) event_control
disable_statement ::=
       disable hierarchical_task_identifier ;
     | disable hierarchical_block_identifier ;
event_control ::=
       @ event_identifier
     | @ ( event_expression )
     | @*
     | @ (*)
event_trigger ::=
       -> hierarchical_event_identifier ;
event_expression ::=
       expression
     | hierarchical_identifier
     | posedge expression
     | negedge expression
     | event_expression or event_expression
     | event_expression , event_expression
procedural_timing_control_statement ::=
       delay_or_event_control statement_or_null
wait_statement ::=
       wait ( expression ) statement_or_null
## A.6.6 Conditional statements
conditional_statement ::=
       if ( expression )
        statement_or_null [ else statement_or_null ]
     | if_else_if_statement
if_else_if_statement ::=
       if ( expression ) statement_or_null
      { else if ( expression ) statement_or_null }
      [ else statement_or_null ]
function_conditional_statement ::=
       if ( expression ) function_statement_or_null
        [ else function_statement_or_null ]
     | function_if_else_if_statement
function_if_else_if_statement ::=
       if ( expression ) function_statement_or_null
      { else if ( expression ) function_statement_or_null }
       [ else function_statement_or_null ]
## A.6.7 Case statements
case_statement ::=
        case ( expression )
        case_item { case_item } endcase
      | casez ( expression )
        case_item { case_item } endcase
      | casex ( expression )
        case_item { case_item } endcase
case_item ::=
        expression { , expression } : statement_or_null
      | default [ : ] statement_or_null
function_case_statement ::=
        case ( expression )
        function_case_item { function_case_item } endcase
      | casez ( expression )
        function_case_item { function_case_item } endcase
      | casex ( expression )
        function_case_item { function_case_item } endcase
function_case_item ::=
        expression { , expression } : function_statement_or_null
      | default [ : ] function_statement_or_null
## A.6.8 Looping statements
function_loop_statement ::=
        forever function_statement
      | repeat ( expression ) function_statement
      | while ( expression ) function_statement
      | for ( variable_assignment ; expression ; variable_assignment )
        function_statement
loop_statement ::=
        forever statement
      | repeat ( expression ) statement
      | while ( expression ) statement
      | for ( variable_assignment ; expression ; variable_assignment )
        statement
## A.6.9 Task enable statements
system_task_enable ::= system_task_identifier [ ( expression { , expression } ) ] ;
task_enable ::= hierarchical_task_identifier [ ( expression { , expression } ) ] ;
# A.7 Specify section
## A.7.1 Specify block declaration
specify_block ::= specify { specify_item } endspecify
specify_item ::=
        specparam_declaration
      | pulsestyle_declaration
      | showcancelled_declaration
      | path_declaration
      | system_timing_check
pulsestyle_declaration ::=
        pulsestyle_onevent list_of_path_outputs ;
     | pulsestyle_ondetect list_of_path_outputs ;
showcancelled_declaration ::=
        showcancelled list_of_path_outputs ;
      | noshowcancelled list_of_path_outputs ;
## A.7.2 Specify path declarations
path_declaration ::=
        simple_path_declaration ;
      | edge_sensitive_path_declaration ;
      | state_dependent_path_declaration ;
simple_path_declaration ::=
        parallel_path_description = path_delay_value
      | full_path_description = path_delay_value
parallel_path_description ::=
      ( specify_input_terminal_descriptor [ polarity_operator ] => specify_output_terminal_descriptor )
full_path_description ::=
      ( list_of_path_inputs [ polarity_operator ] *> list_of_path_outputs )
list_of_path_inputs ::=
        specify_input_terminal_descriptor { , specify_input_terminal_descriptor }
list_of_path_outputs ::=
        specify_output_terminal_descriptor { , specify_output_terminal_descriptor }
## A.7.3 Specify block terminals
specify_input_terminal_descriptor ::=
        input_identifier
      | input_identifier [ constant_expression ]
      | input_identifier [ range_expression ]
specify_output_terminal_descriptor ::=
        output_identifier
      | output_identifier [ constant_expression ]
      | output_identifier [ range_expression ]
input_identifier ::= input_port_identifier | inout_port_identifier
output_identifier ::= output_port_identifier | inout_port_identifier
## A.7.4 Specify path delays
path_delay_value ::=
        list_of_path_delay_expressions
      | ( list_of_path_delay_expressions )
list_of_path_delay_expressions ::=
        t_path_delay_expression
       | trise_path_delay_expression , tfall_path_delay_expression
       | trise_path_delay_expression , tfall_path_delay_expression , tz_path_delay_expression
       | t01_path_delay_expression , t10_path_delay_expression , t0z_path_delay_expression ,
        tz1_path_delay_expression , t1z_path_delay_expression , tz0_path_delay_expression
       | t01_path_delay_expression , t10_path_delay_expression , t0z_path_delay_expression ,
        tz1_path_delay_expression , t1z_path_delay_expression , tz0_path_delay_expression ,
        t0x_path_delay_expression , tx1_path_delay_expression , t1x_path_delay_expression ,
        tx0_path_delay_expression , txz_path_delay_expression , tzx_path_delay_expression
t_path_delay_expression ::= path_delay_expression
trise_path_delay_expression ::= path_delay_expression
tfall_path_delay_expression ::= path_delay_expression
tz_path_delay_expression ::= path_delay_expression
t01_path_delay_expression ::= path_delay_expression
t10_path_delay_expression ::= path_delay_expression
t0z_path_delay_expression ::= path_delay_expression
tz1_path_delay_expression ::= path_delay_expression
t1z_path_delay_expression ::= path_delay_expression
tz0_path_delay_expression ::= path_delay_expression
t0x_path_delay_expression ::= path_delay_expression
tx1_path_delay_expression ::= path_delay_expression
t1x_path_delay_expression ::= path_delay_expression
tx0_path_delay_expression ::= path_delay_expression
txz_path_delay_expression ::= path_delay_expression
tzx_path_delay_expression ::= path_delay_expression
path_delay_expression ::= constant_mintypmax_expression
edge_sensitive_path_declaration ::=
        parallel_edge_sensitive_path_description = path_delay_value
       | full_edge_sensitive_path_description = path_delay_value
parallel_edge_sensitive_path_description ::=
        ( [ edge_identifier ] specify_input_terminal_descriptor =>
        specify_output_terminal_descriptor [ polarity_operator ] : data_source_expression )
full_edge_sensitive_path_description ::=
        ( [ edge_identifier ] list_of_path_inputs *>
        list_of_path_outputs [ polarity_operator ] : data_source_expression )
data_source_expression ::= expression
edge_identifier ::= posedge | negedge
state_dependent_path_declaration ::=
        if ( module_path_expression ) simple_path_declaration
       | if ( module_path_expression ) edge_sensitive_path_declaration
       | ifnone simple_path_declaration
 polarity_operator ::= + | -
## A.7.5 System timing checks
### A.7.5.1 System timing check commands
system_timing_check ::=
       $setup_timing_check
     | $hold _timing_check
     | $setuphold_timing_check
     | $recovery_timing_check
     | $removal_timing_check
     | $recrem_timing_check
     | $skew_timing_check
     | $timeskew_timing_check
     | $fullskew_timing_check
     | $period_timing_check
     | $width_timing_check
     | $nochange_timing_check
$setup_timing_check ::=
       $setup ( data_event , reference_event , timing_check_limit [ , [ notify_reg ] ] ) ;
$hold _timing_check ::=
       $hold ( reference_event , data_event , timing_check_limit [ , [ notify_reg ] ] ) ;
$setuphold_timing_check ::=
       $setuphold ( reference_event , data_event , timing_check_limit , timing_check_limit
        [ , [ notify_reg ] [ , [ stamptime_condition ] [ , [ checktime_condition ]
        [ , [ delayed_reference ] [ , [ delayed_data ] ] ] ] ] ] ) ;
$recovery_timing_check ::=
       $recovery ( reference_event , data_event , timing_check_limit [ , [ notify_reg ] ] ) ;
$removal_timing_check ::=
       $removal ( reference_event , data_event , timing_check_limit [ , [ notify_reg ] ] ) ;
$recrem_timing_check ::=

       $recrem ( reference_event , data_event , timing_check_limit , timing_check_limit
        [ , [ notify_reg ] [ , [ stamptime_condition ] [ , [ checktime_condition ]
        [ , [ delayed_reference ] [ , [ delayed_data ] ] ] ] ] ] ) ;
$skew_timing_check ::=
       $skew ( reference_event , data_event , timing_check_limit [ , [ notify_reg ] ] ) ;
$timeskew_timing_check ::=
       $timeskew ( reference_event , data_event , timing_check_limit
        [ , [ notify_reg ] [ , [ event_based_flag ] [ , [ remain_active_flag ] ] ] ] ) ;
$fullskew_timing_check ::=
       $fullskew ( reference_event , data_event , timing_check_limit , timing_check_limit
        [ , [ notify_reg ] [ , [ event_based_flag ] [ , [ remain_active_flag ] ] ] ] ) ;
$period_timing_check ::=
       $period ( controlled_reference_event , timing_check_limit [ , [ notify_reg ] ] ) ;
$width_timing_check ::=
       $width ( controlled_reference_event , timing_check_limit ,
        threshold [ , [ notify_reg ] ] ) ;
$nochange_timing_check ::=
       $nochange ( reference_event , data_event , start_edge_offset ,
        end_edge_offset [ , [ notify_reg ] ] ) ;
### A.7.5.2 System timing check command arguments
checktime_condition ::= mintypmax_expression
controlled_reference_event ::= controlled_timing_check_event
data_event ::= timing_check_event
delayed_data ::=
        terminal_identifier
       | terminal_identifier [ constant_mintypmax_expression ]
delayed_reference ::=
        terminal_identifier
       | terminal_identifier [ constant_mintypmax_expression ]
end_edge_offset ::= mintypmax_expression
event_based_flag ::= constant_expression
notify_reg ::= variable_identifier
reference_event ::= timing_check_event
remain_active_flag ::= constant_mintypmax_expression
stamptime_condition ::= mintypmax_expression
start_edge_offset ::= mintypmax_expression
threshold ::=constant_expression
timing_check_limit ::= expression
### A.7.5.3 System timing check event definitions
timing_check_event ::=
        [timing_check_event_control] specify_terminal_descriptor [ &&& timing_check_condition ]
controlled_timing_check_event ::=
        timing_check_event_control specify_terminal_descriptor [ &&& timing_check_condition ]
timing_check_event_control ::=
        posedge
       | negedge
       | edge_control_specifier
specify_terminal_descriptor ::=
        specify_input_terminal_descriptor
       | specify_output_terminal_descriptor
edge_control_specifier ::= edge [ edge_descriptor [ , edge_descriptor ] ]
edge_descriptor1 ::=
        01
       | 10
       | z_or_x zero_or_one
       | zero_or_one z_or_x
zero_or_one ::= 0 | 1
z_or_x ::= x | X | z | Z
timing_check_condition ::=
        scalar_timing_check_condition
       | ( scalar_timing_check_condition )
scalar_timing_check_condition ::=
       expression
     | ~ expression
     | expression == scalar_constant
     | expression === scalar_constant
     | expression != scalar_constant
     | expression !== scalar_constant
scalar_constant ::=
       1’b0 | 1’b1 | 1’B0 | 1’B1 | ’b0 | ’b1 | ’B0 | ’B1 | 1 | 0
# A.8 Expressions
## A.8.1 Concatenations
concatenation ::= { expression { , expression } }
constant_concatenation ::= { constant_expression { , constant_expression } }
constant_multiple_concatenation ::= { constant_expression constant_concatenation }
module_path_concatenation ::= { module_path_expression { , module_path_expression } }
module_path_multiple_concatenation ::= { constant_expression module_path_concatenation }
multiple_concatenation ::= { constant_expression concatenation }
net_concatenation ::= { net_concatenation_value { , net_concatenation_value } }
net_concatenation_value ::=
       hierarchical_net_identifier
     | hierarchical_net_identifier [ expression ] { [ expression ] }
     | hierarchical_net_identifier [ expression ] { [ expression ] } [ range_expression ]
     | hierarchical_net_identifier [ range_expression ]
     | net_concatenation
variable_concatenation ::= { variable_concatenation_value { , variable_concatenation_value } }
variable_concatenation_value ::=
       hierarchical_variable_identifier
     | hierarchical_variable_identifier [ expression ] { [ expression ] }
     | hierarchical_variable_identifier [ expression ] { [ expression ] } [ range_expression ]
     | hierarchical_variable_identifier [ range_expression ]
     | variable_concatenation
## A.8.2 Function calls
constant_function_call ::= function_identifier { attribute_instance }
        ( constant_expression { , constant_expression } )
function_call ::= hierarchical_function_identifier{ attribute_instance }
        ( expression { , expression } )
genvar_function_call ::= genvar_function_identifier { attribute_instance }
        ( constant_expression { , constant_expression } )
system_function_call ::= system_function_identifier
        [ ( expression { , expression } ) ]
## A.8.3 Expressions
base_expression ::= expression
conditional_expression ::= expression1 ? { attribute_instance } expression2 : expression3
constant_base_expression ::= constant_expression
constant_expression ::=
        constant_primary
      | unary_operator { attribute_instance } constant_primary
      | constant_expression binary_operator { attribute_instance } constant_expression
      | constant_expression ? { attribute_instance } constant_expression : constant_expression
      | string
constant_mintypmax_expression ::=
        constant_expression
      | constant_expression : constant_expression : constant_expression
constant_range_expression ::=
        constant_expression
      | msb_constant_expression : lsb_constant_expression
      | constant_base_expression +: width_constant_expression
      | constant_base_expression -: width_constant_expression
dimension_constant_expression ::= constant_expression
expression1 ::= expression
expression2 ::= expression
expression3 ::= expression
expression ::=
        primary
      | unary_operator { attribute_instance } primary
      | expression binary_operator { attribute_instance } expression
      | conditional_expression
      | string
lsb_constant_expression ::= constant_expression
mintypmax_expression ::=
        expression
      | expression : expression : expression
module_path_conditional_expression ::= module_path_expression ? { attribute_instance }
        module_path_expression : module_path_expression
module_path_expression ::=
        module_path_primary
      | unary_module_path_operator { attribute_instance } module_path_primary
 | module_path_expression binary_module_path_operator { attribute_instance }
        module_path_expression
      | module_path_conditional_expression
module_path_mintypmax_expression ::=
        module_path_expression
      | module_path_expression : module_path_expression : module_path_expression
msb_constant_expression ::= constant_expression
range_expression ::=
        expression
      | msb_constant_expression : lsb_constant_expression
      | base_expression +: width_constant_expression
      | base_expression -: width_constant_expression
width_constant_expression ::= constant_expression
## A.8.4 Primaries
constant_primary ::=
       constant_concatenation
     | constant_function_call
     | ( constant_mintypmax_expression )
     | constant_multiple_concatenation
     | genvar_identifier
     | number
     | parameter_identifier
     | specparam_identifier
module_path_primary ::=
       number
     | identifier
     | module_path_concatenation
     | module_path_multiple_concatenation
     | function_call
     | system_function_call
     | constant_function_call
     | ( module_path_mintypmax_expression )
primary ::=
       number
     | hierarchical_identifier
     | hierarchical_identifier [ expression ] { [ expression ] }
     | hierarchical_identifier [ expression ] { [ expression ] } [ range_expression ]
     | hierarchical_identifier [ range_expression ]
     | concatenation
     | multiple_concatenation
     | function_call
     | system_function_call
     | constant_function_call
     | ( mintypmax_expression )
## A.8.5 Expression left-side values
net_lvalue ::=
       hierarchical_net_identifier
     | hierarchical_net_identifier [ constant_expression ] { [ constant_expression ] }
     | hierarchical_net_identifier [ constant_expression ] { [ constant_expression ] } [
        constant_range_expression ]
     | hierarchical_net_identifier [ constant_range_expression ]
     | net_concatenation
variable_lvalue ::=
       hierarchical_variable_identifier
     | hierarchical_variable_identifier [ expression ] { [ expression ] }
     | hierarchical_variable_identifier [ expression ] { [ expression ] } [ range_expression ]
     | hierarchical_variable_identifier [ range_expression ]
     | variable_concatenation
## A.8.6 Operators
unary_operator ::=
        + | - | ! | ~ | & | ~& | | | ~| | ^ | ~^ | ^~
binary_operator ::=
        + | - | * | / | % | == | != | === | !== | && | || | **
       | < | <= | > | >= | & | | | ^ | ^~ | ~^ | >> | << | >>> | <<<
unary_module_path_operator ::=
        ! | ~ | & | ~& | | | ~| | ^ | ~^ | ^~
binary_module_path_operator ::=
        == | != | && | || | & | | | ^ | ^~ | ~^
## A.8.7 Numbers
number ::=
        decimal_number
       | octal_number
       | binary_number
       | hex_number
       | real_number
real_number1 ::=
        unsigned_number . unsigned_number
       | unsigned_number [ . unsigned_number ] exp [ sign ] unsigned_number
exp ::= e | E
decimal_number ::=
        unsigned_number
       | [ size ] decimal_base unsigned_number
       | [ size ] decimal_base x_digit { _ }
       | [ size ] decimal_base z_digit { _ }
binary_number ::= [ size ] binary_base binary_value
octal_number ::= [ size ] octal_base octal_value
hex_number ::= [ size ] hex_base hex_value
sign ::= + | -
size ::= non_zero_unsigned_number
non_zero_unsigned_number1 ::= non_zero_decimal_digit { _ | decimal_digit}
unsigned_number1 ::= decimal_digit { _ | decimal_digit }
binary_value1 ::= binary_digit { _ | binary_digit }
octal_value1 ::= octal_digit { _ | octal_digit }
hex_value1 ::= hex_digit { _ | hex_digit }
decimal_base1 ::= ’[s|S]d | ’[s|S]D
binary_base1 ::= ’[s|S]b | ’[s|S]B
octal_base1 ::= ’[s|S]o | ’[s|S]O
hex_base1 ::= ’[s|S]h | ’[s|S]H
non_zero_decimal_digit ::= 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
decimal_digit ::= 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
binary_digit ::= x_digit | z_digit | 0 | 1
octal_digit ::= x_digit | z_digit | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
hex_digit ::=
        x_digit | z_digit | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
      |a|b|c|d|e|f|A|B|C|D|E|F
x_digit ::= x | X
z_digit ::= z | Z | ?
## A.8.8 Strings
string ::= " { Any_ASCII_Characters_except_new_line } "
# A.9 General
## A.9.1 Attributes
attribute_instance ::= (* attr_spec { , attr_spec } *)
attr_spec ::=
        attr_name = constant_expression
      | attr_name
attr_name ::= identifier
## A.9.2 Comments
comment ::=
        one_line_comment
      | block_comment
one_line_comment ::= // comment_text \n
block_comment ::= /* comment_text */
comment_text ::= { Any_ASCII_character }
A.9.3 Identifiers
arrayed_identifier ::=
        simple_arrayed_identifier
      | escaped_arrayed_identifier
block_identifier ::= identifier
cell_identifier ::= identifier
config_identifier ::= identifier
escaped_arrayed_identifier ::= escaped_identifier [ range ]
escaped_hierarchical_identifier4 ::=
        escaped_hierarchical_branch
        { .simple_hierarchical_branch | .escaped_hierarchical_branch }
escaped_identifier ::= \ {Any_ASCII_character_except_white_space} white_space
event_identifier ::= identifier
function_identifier ::= identifier
gate_instance_identifier ::= arrayed_identifier
generate_block_identifier ::= identifier
genvar_function_identifier ::= identifier /* Hierarchy disallowed */
genvar_identifier ::= identifier
hierarchical_block_identifier ::= hierarchical_identifier
hierarchical_event_identifier ::= hierarchical_identifier
hierarchical_function_identifier ::= hierarchical_identifier
hierarchical_identifier ::=
        simple_hierarchical_identifier
       | escaped_hierarchical_identifier
hierarchical_net_identifier ::= hierarchical_identifier
hierarchical_variable_identifier ::= hierarchical_identifier
hierarchical_task_identifier ::= hierarchical_identifier
identifier ::=
        simple_identifier
       | escaped_identifier
inout_port_identifier ::= identifier
input_port_identifier ::= identifier
instance_identifier ::= identifier
library_identifier ::= identifier
memory_identifier ::= identifier
module_identifier ::= identifier
module_instance_identifier ::= arrayed_identifier
net_identifier ::= identifier
output_port_identifier ::= identifier
parameter_identifier ::= identifier
port_identifier ::= identifier
real_identifier ::= identifier
simple_arrayed_identifier ::= simple_identifier [ range ]
simple_hierarchical_identifier3 ::=
        simple_hierarchical_branch [ .escaped_identifier ]
simple_identifier2 ::= [ a-zA-Z_ ] { [ a-zA-Z0-9_$ ] }
specparam_identifier ::= identifier
system_function_identifier5 ::= $[ a-zA-Z0-9_$ ]{ [ a-zA-Z0-9_$ ] }
system_task_identifier5 ::= $[ a-zA-Z0-9_$ ]{ [ a-zA-Z0-9_$ ] }
task_identifier ::= identifier
terminal_identifier ::= identifier
text_macro_identifier ::= simple_identifier
topmodule_identifier ::= identifier
udp_identifier ::= identifier
udp_instance_identifier ::= arrayed_identifier
variable_identifier ::= identifier
## A.9.4 Identifier branches
simple_hierarchical_branch3 ::=
        simple_identifier [ [ unsigned_number ] ]
        [ { .simple_identifier [ [ unsigned_number ] ] } ]
escaped_hierarchical_branch4 ::=
        escaped_identifier [ [ unsigned_number ] ]
        [ { .escaped_identifier [ [ unsigned_number ] ] } ]
## A.9.5 White space
white_space ::= space | tab | newline | eof6
# NOTES
       1) Embedded spaces are illegal.
       2) A simple_identifier and arrayed_reference shall start with an alpha or underscore (_) character,
        shall have at least one character, and shall not have any spaces.
       3) The period (.) in simple_hierarchical_identifier and simple_hierarchical_
        branch shall not be preceded or followed by white_space.
       4) The period in escaped_hierarchical_identifier and escaped_hierarchical_
        branch shall be preceded by white_space, but shall not be followed by white_space.
       5) The $ character in a system_function_identifier or system_task_identifier shall not be followed
        by white_space. A system_function_identifier or system_task_identifier shall not be escaped.
       6) End of file.

## KEY
posedge	Outlined words and characters are Literals & Keywords